## Slide 1: East Area Secondary Beam Control User Guide Revised version after LS1
L.Gatignon / EN-MEF
5 January 2015

## Slide 2: From where
The East Area secondary beam lines are controlled from the EBCR. This room is located on the first floor, above the T10 control room, downstream of the T11 area. You can access this room easily from the big gate (Porte 18) on the Bldg 251/252 side.
Many beam elements can be controlled from the user control rooms.

## Slide 3: Tools for Beam Control
There is a PC for magnet control (both beam and spectrometer magnets) and detector readout
A series of racks allows to control collimators, vacuum, access signals from the barracks and get timing signals

## Slide 4
COLLIMATORS
For users:
For experts:
VACUUM CONTROL
DRIFT CHAMBERS

## Slide 5: TIMING AND OTHER SIGNALS
Communication with user barracks
Communication with APRON (primary beam electronics and RP barrack)
Timing distribution
Two more racks provide timing signals and connections with the user barracks

## Slide 6: Magnet and detector control
Magnets and detectors are controlled from the CESAR beam control program.
The use of Cesar is described in the Control Summary Sheets (quick User Guide: http://sba.web.cern.ch/sba/Documentations/docs/Controls-Summary-Sheet.pdf also available as plastified sheets in the EBCR.
Folder with reference
settings and general info
Beam control PC (user: eaop
passwd: . . . . . . . . )
Magnets and detectors are controlled and read from the Linux PC in the EBCR or from the beam computers in the user control rooms

## Slide 7: Magnets: Which current?
Lists of currents for each energy are available in the green folder. Whenever you change energy, all currents must be modified using the knobs. Normally the sign of the current corresponds to the sign of the beam particles (except possibly for ZT9.QFO03 – ask your liaison physicist)
Please check carefully that you are changing the right rectifier in the right beam! (In each knob the name of the magnet contains the name of its beam line, e.g. ZT9.BHZ1)
Do not use the currents in the old printed User manuals. They are obsolete.
Please consult the liaison physicist if you have special beam requirements, e.g. different focusing of the beam.

## Slide 8: Collimator control
Find the crate controlling the collimators in your beam line
If you want to open to (-x, +y) mm, dial 50+x/2 and 50+y/2 with the thumbwheels
Push on the red STROBE buttons
The final position in mm is shown on the LCD screens. Push STROBE again if the setting reached is not precise enough.
The horizontal collimators usually define Dp/p with typically Dp/p=±1% for ±5 mm gap (see User manual). The vertical collimators control the angular acceptance and hence the beam flux and the divergence at your detector. Check in the green folder
x
y
Thumbwheels
LCD screens

## Slide 9: Vacuum control
The vacuum control is regularly checked by experts from the AT/VAC group.
However, the user can check the vacuum in his beam line in case of problems.
Typical values are in the few 10-2 mbar ballpark

## Slide 10: TIMING SIGNALS
The detailed documentation is available in the paper document inside the module
The North branch (T9, T10, T11) uses EASTA cycles, the T7 line and IRRAD the EASTC cycles. DIRAC uses EASTB.
Paper documentation
Select the wanted cycles
Delay (in msec) from start of PS cycle
Signal during full PS cycles selected
Pulse at start of extraction ( delay)

## Slide 11: Communication with barracks
There are several cable connections between the user barracks and the EBCR. The name of the barrack is written on the blue panels above each patch panel.
Please check the labels for the correspondence between the barrack and EBCR connectors

## Slide 12: Information from the PS machine
Activate EA Vistar from the
General menu in the Java Console Manager:
The green dots indicate the
Intensity per spill for the different
Target telescopes
The white curve shows
The shape of the spill over
Its 400 msec length

## Slide 13
The Vistar on the TV screen shows the overall state of the PS (+ cycles):
Magnet current
Inst. Intensity
Active cycle
Cycle intensity
Comments from
the operators

## Slide 14: Further Information
There is a web page: http://cern.ch/gatignon/EastArea
The access system operation is described in http://cern.ch/gatignon/EastArea/Access.html
Call the CCC (76677) for operational problems (24 hrs/day, 7 days/week)
Call your liaison physicist (L.Gatignon, 163554) for other questions and requests (during working hours)